## Slide 1
Furniture Joints

## Slide 2: Butt Joints
A butt joint is made when two pieces of wood are butted together and glued.
End grain to side grain is not very strong

## Slide 3: Name These Edge Joints
a
b
c
d
Can you draw a Comb joint, Tongue & Groove or Slotted screw joint.
Rubbed glue joint
Dowel joint
Biscuit joint
Loose tongue joint

## Slide 4: Section through board widening joints.
Scarf Joints
A : Rubbed Glue Joint
B : Tongue & Groove Joint
C : Biscuit Joint
D : Loose Tongue
E : Dowel Joint

## Slide 5: Modern Comb joint
Cutters used in table router

## Slide 6: Having / Lap joints
Lap joints are created when two pieces of wood overlap one another at a right angle. Very simple form of jointing.
Can you name another type of having?

## Slide 7: Bridle Joints
The bridle joint is a simple joint. Material is usually divided into thirds.
Corner Bridle
Tee Bridle

## Slide 8: Mortise & Tenon
The mortise and tenon joint is one of the strongest traditional furniture joints. Usually found on good quality furniture.
It was sometimes reinforced with wedges, pegs or keys.
Lots of variations of these joints based on material being jointed and function of joint.
Barefaced tenon only has one shoulder used for connecting a narrow rail to a leg.
Barefaced tenon

## Slide 9: Mortise & Tenon
The haunch helps prevent the wider rails from twisting as it is fitted into the groove used mainly on panelled doors.
The high and low shoulder or long and short shoulder is used on rebated frames such as mirror or picture frames or window frames.
Haunched M & T
High & Low Shoulder
M & T

## Slide 10: Mortise & Tenon
The scribed M&T used on Kitchen & Wardrobe doors. The components are machined using cutters. A larger scribed M&T can be carried out on the double ended tennoner for large panelled doors.
The mitred M&T is also used on rebated frames such as mirror or picture frames and cabinet doors. The material is removed to allow for a straight shoulder.
Scribed M & T
Mitred M & T

## Slide 11: Keyed Mortice and Tenon

## Slide 12: Craftsmanspace Free technical plans, books, patterns, software
http://www.craftsmanspace.com/knowledge/keyed-mortise-and-tenon-joint.html
How to mark out a Key

## Slide 13: Corner Mitre Joints
The mitre joint usually cut at 45 degrees, on the ends of two pieces of wood, used on frames.
Can you name this bottom joint
Mitred bridle joint

## Slide 14: Housing joints
Jointing across the width shelf to side.
Can you draw a rebate housing & dovetail housing

## Slide 15: Dovetails
The dovetail joint is one of the most distinctive and best antique furniture joints used in furniture construction to join wood at a right angle.
Recognised by the angled pieces that replicate doves’ tails.
They form a strong interlockable joint with a large gluing area.
Used for joining carcass ends and for creating drawers.
Wide variations available, used as features on high class furniture.

## Slide 16: Carcase Joints
Through Dovetail
Lapped Dovetail
Secret Mitre Dovetail
Double Lapped
Dovetail
Through Pinned
Joint
Finger Joint

## Slide 17: Rule Joint
Rule joint hinge. Image from
woodworkersjournal.com
This joint is used on drop leaf tables. The rule joint is jointed
together using a rule joint hinge. The hinge has one leaf
longer than the other why?

## Slide 18: Knuckle Joint
Traditional moveable joint used on drop leaf tables

## Slide 19: Trend 9/41 Knuckle Joint Cutter
Note: Cutter should be used in router table

## Slide 20: Quick Test
What have you learned so far?
See if you can correctly name each joint before progressing onto the next slide.

## Slide 21: Can You Name these joints

## Slide 22: Can You Name these joints
Scarf Joints
A : Rubbed Glue Joint
B : Tongue & Groove Joint
C : Biscuit Joint
D : Loose Tongue
E : Dowel Joint

## Slide 23: Can You Name these joints

## Slide 24: Can You Name these joints
1 Bridle joint
2 Barefaced M & T
3 Scribed M & T
4 Mitred M & T
5 High & Low Shoulder
M & T
6 Fox wedged M & T
8 Corner Mitred
Bridle joint
7 Haunched M & T
9 Twin Tenon

## Slide 25: Can You Name these joints

## Slide 26: Can You Name these joints
Tennoned &
mitred clamped
Rule joint
Projected wedged
mortise & tenon
Knuckle joint
Dovetail Key
Housing joint

## Slide 27: Can You Name these joints

## Slide 28: Can You Name these joints
Hammer Head
Tenon joint
Machine Dovetails
Dovetail Halving
Stopped Housing
Stopped Dovetail
Housing
Bridle Joint

## Slide 29: Modern Jointing
Using machines and jigs.
Click link to bring you to video demonstration.

## Slide 30: Modern Jointing

## Slide 31: Dowels
Dowel are a fast way of jointing.
Holes need to be aligned accurately.
Different patterns are available that allow glue to spread.

## Slide 32: Biscuits
Biscuits are a faster way of jointing, small allowance for accuracy.

## Slide 33: Domino
Cross between a dowel and a biscuit you get a domino tennon.
Festool domino joiner

## Slide 34: Beadlock Pro
Alternative to the mortice and tennon something similar to using a false tennon.
Using jig drill a series of holes to match width of bead.

## Slide 35: JessEm Slip slot mortise mill
http://www.youtube.com/watch?v=_VtVGnxlBrc
This is based on false tenons. It is a jig and custom made
drill bit that can be used in any handheld drill.